## Slide 1: Quality Management
Tips & Points to Remember

## Slide 2: Quality Management
Quality | Conformance to requirements and fitness to use
Quality Management | Processes required to ensure that the project will satisfy the needs or which it was undertaken
Continuous Improvement (Kaizen) | Small Improvements in products and processes to reduce costs and ensure consistency of performance of products and services.
Just in Time | Decreases the amount of inventory; forces zero defects
ISO 9000 | Helps to ensure that organizations have quality procedures and that they follow them
TQM | Encourages companies and employees to focus on finding ways to continuously improve quality
Prevention over inspection | Quality must be planned in, not inspected in Prevention: Keeping errors out of the process Inspection: Keeping the errors out of the hands of the customer

## Slide 3: Quality Management
Normal Distribution | Most common probability density distribution chart; bell curve; used to measure variations
Standard Deviation (Sigma or σ) | Measure of how far the deviation is from the mean. ±1σ = 68.26% ±2σ = 95.46% ±3σ = 99.73% ±6σ = 99.99%
Responsibility | Ultimate : Employee Overall or Primary : Project Manager Primary Resp. for establishing design & test specs : Engineer
Pareto Diagram | 80-20 rule; Prioritization of potential causes Separate critical few from the uncritical many Order of priority and focus attention on the most critical

## Slide 4: Quality Management
Control Chart | Graphic Displays of results used to determine if the process is in control UCL, LCL,Mean Specification Limit : Customer’s expectations or contractual requirements Rule of Seven : 7 points on the same side (Probability = 0.0078)
Checksheets/lists | List of items/picture of item to be inspected
Fishbone/Ishikawa/ Cause-and-Effect | Creative way to investigate root cause Helps simulate thinking, organizes thoughts and generates discussion Can be used to explore a desired future outcome and the factors to which it relates
Trend Analysis | Technical Performance : Errors identified; remain uncorrected Cost & Schedule : How many activities per period was completed with significant variances

## Slide 5: Quality Management
Quality Policy | Overall intentions and direction of an organization with regard to quality as formally expressed by top management.
Cost of conformance | Training, Studies, Survey etc
Cost of non-conformance | Rework, Scrap, Warranty Costs, Inventory Costs etc
Sampling | Attribute Sampling : Result conforms or not Variable Sampling : Result on a continous scale that measures the degree of conformity